## Slide 1
Team Chipsters
FEASIBILITY AND VIABILITY
@SIH Idea submission- Template 4
1. TECHNICAL & SILICON FEASIBILITY (PROVEN IN RTL)
• Pure-Logic RTL (Zero DSP / 0 BRAM): Eliminates high-cost FPGA components; synthesizes entirely into standard LUT logic.
• Minimal Silicon Utilization: Consumes only ~40% LUT5s and ~30% flip-flops on ultra-low-cost Renesas ForgeFPGA (SLG47910C).
• Multi-Vendor Code Portability: Identical synthesizable Verilog compiles seamlessly on AMD Xilinx (6-LUT) and Renesas (5-LUT).
• Static Timing Closure (+5.603 ns WNS): Validated in Vivado ML at 50 MHz clock; verified operational ceiling of 69.45 MHz.
2. FINANCIAL & COMMERCIAL VIABILITY (UNIT ECONOMICS)
• Prototype Single-Unit BOM: ₹3,500 (~$40 retail) for custom FPGA carrier + ESP32-S3 + multi-sensor cluster.
• Mass-Production Bulk Target (<$18 / ₹1,450): Micro-FPGA ($1.80) + ESP32 ($2.20) + Sensors ($5.80) + Battery/Enclosure ($4.20).
• Zero Ongoing Cloud Cost: 100% on-device TinyML edge execution = ₹0 cloud server or API subscription cost per user.
• 95% Cost Reduction vs Wearables: Delivers hospital-grade mNEWS2 triage at ₹1,450 vs commercial monitors at ₹25k–₹40k.
3. OPERATIONAL CHALLENGES & MITIGATION MATRIX
Operational Challenge | Engineering Mitigation | Proven Result
PPG Motion Artifacts | 8-Tap MA Filter + Peak FSM | 250ms refractory lockout
Micro-FPGA Capacity | O(1) Bit-Shift Division (>>3) | 0 DSP, 0 BRAM used
FPGA Pin Constraints | 4-Bit Clock-Strobed Bus | Saves 12 GPIO pins
Network Outages | 100% Autonomous Edge TinyML | 619-byte offline model
4. VALIDATION & SCALABLE DEPLOYMENT ROADMAP
• Phase 1: Lab Silicon Validation [COMPLETED]: Hardware prototype tested on Renesas ForgeFPGA + ESP32-S3. Benchmarked on 16k+ MIMIC-III patient records (94.11% accuracy).
• Phase 2: Pilot Field Deployment [NEAR-TERM]: 50-unit pilot trial targeting municipal sanitation workers, traffic police, and construction sites under 45°C heat.
• Phase 3: Commercial Silicon Target [MASS SCALE]: Direct migration of Verilog DSP to Qualcomm Hexagon DSP; TinyML deployed to Qualcomm NPU via Snapdragon Neural Processing SDK (SNPE).