## Slide 1
SHRIKEFI SYSTEM ARCHITECTURE & DATA FLOW
End-to-End Edge Pipeline: Sensor Acquisition -> 50 MHz FPGA Filtering -> Clinical TinyML -> Autonomous Action
STAGE 01
Sensing Layer
PHYSICAL DATA ACQUISITION
• MAX30102 PPG Sensor
Dual Red & IR optical pulse oximeter measuring pulsatile arterial blood flow and SpO2 levels.
• BME280 Climate Sensor
Calibrated digital sensor measuring ambient temperature, humidity & barometric pressure.
• PMSA003 PM2.5 Sensor
Laser scattering particulate sensor measuring hazardous airborne PM1.0, PM2.5, and PM10.
I2C / UART Raw ADC
STAGE 02
FPGA RTL Core
50 MHZ CUSTOM SILICON
• Dual 8-Tap Filter
O(1) running-sum MA noise filter with bit-shift division (>> 3). Consumes 0 DSP slices and 0 BRAM.
• Systolic Peak FSM
4-state finite state machine with a 250 ms refractory lock-out window preventing false dicrotic double-peaks.
• 20 ns Cycle Timer
Continuous 50 MHz cycle counter latching inter-beat intervals (IBI) with 0 software jitter.
4-Bit Link 20ns IBI
STAGE 03
Clinical TinyML
ESP32-S3 DUAL-CORE
• mNEWS2 Triage Engine
Royal College of Physicians early warning clinical triage protocol for acute vital deterioration.
• Karlen / Elgendi SQI
Multi-parameter Signal Quality Index evaluating skewness & perfusion, rejecting motion artifacts.
• 6->24->16->3 Model
619-parameter INT8 neural net; 94.11% MIMIC-III benchmarked with Absolute Crisis Override safety.
Vitals Sync Risk Tiers
STAGE 04
Output & Action
EDGE ALERTS & TELEMETRY
• OLED Local Display
128x64 high-contrast zero-latency screen showing real-time HR, SpO2, RR, and threat tiers.
• WiFi / MQTT Telemetry
Secure real-time bidirectional telemetry streaming to hospital command and IoT backends.
• 60 FPS Win32 GUI
Hardware-accelerated GDI desktop oscilloscope for multi-sensor waveforms and live telemetry.
CORE BENCHMARKS: 50 MHz FPGA Clock (20 ns IBI) | 0 DSP / 0 BRAM RTL | 94.11% MIMIC-III Clinical Accuracy | Sub-5ms Triage Latency

## Slide 2
SHRIKEFI SYSTEM ARCHITECTURE & DATA FLOW
End-to-End Edge Pipeline: Sensor Acquisition -> 50 MHz FPGA Filtering -> Clinical TinyML -> Autonomous Action
STAGE 01
Sensing Layer
PHYSICAL DATA ACQUISITION
• MAX30102 PPG Sensor
Dual Red & IR optical pulse oximeter measuring pulsatile arterial blood flow and SpO2 levels.
• BME280 Climate Sensor
Calibrated digital sensor measuring ambient temperature, humidity & barometric pressure.
• PMSA003 PM2.5 Sensor
Laser scattering particulate sensor measuring hazardous airborne PM1.0, PM2.5, and PM10.
I2C / UART Raw ADC
STAGE 02
FPGA RTL Core
50 MHZ CUSTOM SILICON
• Dual 8-Tap Filter
O(1) running-sum MA noise filter with bit-shift division (>> 3). Consumes 0 DSP slices and 0 BRAM.
• Systolic Peak FSM
4-state finite state machine with a 250 ms refractory lock-out window preventing false dicrotic double-peaks.
• 20 ns Cycle Timer
Continuous 50 MHz cycle counter latching inter-beat intervals (IBI) with 0 software jitter.
4-Bit Link 20ns IBI
STAGE 03
Clinical TinyML
ESP32-S3 DUAL-CORE
• mNEWS2 Triage Engine
Royal College of Physicians early warning clinical triage protocol for acute vital deterioration.
• Karlen / Elgendi SQI
Multi-parameter Signal Quality Index evaluating skewness & perfusion, rejecting motion artifacts.
• 6->24->16->3 Model
619-parameter INT8 neural net; 94.11% MIMIC-III benchmarked with Absolute Crisis Override safety.
Vitals Sync Risk Tiers
STAGE 04
Output & Action
EDGE ALERTS & TELEMETRY
• OLED Local Display
128x64 high-contrast zero-latency screen showing real-time HR, SpO2, RR, and threat tiers.
• WiFi / MQTT Telemetry
Secure real-time bidirectional telemetry streaming to hospital command and IoT backends.
• 60 FPS Win32 GUI
Hardware-accelerated GDI desktop oscilloscope for multi-sensor waveforms and live telemetry.
CORE BENCHMARKS: 50 MHz FPGA Clock (20 ns IBI) | 0 DSP / 0 BRAM RTL | 94.11% MIMIC-III Clinical Accuracy | Sub-5ms Triage Latency